VTS服务指南

–（中国）–（珠海交管中心）

一、VHF程序

（一）分区

珠海交管中心VTS覆盖区分为以下一个分区：

分区              工作频道

珠海              呼叫/守听频道：VHF CH13

业务通话频道：VHF CH68、CH08

船舶应呼叫珠海交管中心，并必须在相应VHF频道上保持守听。

（二）其他频道

拖船         VHF CH16、CH13

引航         VHF CH16、CH13

（三）珠海VTS区域

珠海VTS区域范围是下列船舶报告线与岸线之间的水域：

1.西报告线：自点21°45′00″N/113°07′00″E沿113°07′00″E经线向北至岸线；

2.南报告线：自点21°45′00″N/113°07′00″E沿21°45′00″N纬线向东至点21°45′00″N/113°27′00″E；

3.东报告线：自点21°45′00″N/113°27′00″E沿113°27′00″E经线向北至点21°59′00″N/113°27′00″E；

4.北报告线：21°54′00″N/113°16′00″E与21°59′00″N/113°27′00″E连线。

二、船舶报告

（一）适用船舶

珠海交管中心适用于：

1.外国籍船舶、设施；

2.500总吨及以上的中国籍船舶；

3.载客能力30人及以上的客船；

4.载运危险货物的船舶；

5.操纵能力受到限制的船舶。

（二）预报(仅适用于1000总吨及以上的船舶)

1.报告时机：进入服务区前24小时（航程不足24小时的，在离开上一港口时）。

2.报告：珠海交管中心

3.报告方式：电子邮件、传真或网上填报等形式通知珠海VTS中心

4.报告内容：见《VTS船舶动态计划预报表》。

（三）进港报告

1.报告时机：通过报告线（点）和/或抵近泊位或者锚地；LNG船舶抵达VTS报告线前2小时应当向VTS中心报告抵港时间。

2.报告：珠海交管中心

3.报告方式：VHF CH13

4.报告内容：船舶（船名、呼号）、最大吃水、船位等。

（四）抵港报告

1.报告时机：船舶抵达VTS覆盖区内泊位、浮筒或者锚地。

2.报告：珠海交管中心

3.报告方式：VHF CH13

4.报告内容：船舶（船名、呼号）、时间、船位等。

（五）开航报告

1.报告时机：船舶离泊、离开浮筒或起锚前。

2.报告：珠海交管中心

3.报告方式：VHF CH13

4.报告内容：船舶（船名、呼号）、时间、船位、最大吃水及目的港等。

（六）离港报告

1.报告时机：船舶通过报告线离开VTS覆盖区。

2.报告：珠海交管中心

3.报告方式：VHF CH13

4.报告内容：船舶（船名、呼号）、时间(通过报告线时间)、船位及目的港等。

（七）变化报告

1.报告时机：船舶预报计划信息发生变化。

2.报告：珠海交管中心

3.报告方式：VHF CH13

4.报告内容：变化的项目。

（八）事故报告

1.报告时机：船舶发生影响交通安全和环境污染事故。

2.报告：珠海交管中心

3.报告方式：VHF CH13

4.报告内容：事故细节。

（九）异常情况报告

1.报告时机：发现妨碍航行安全的异常情况。

2.报告：珠海交管中心

3.报告方式：VHF CH13

4.报告内容：船舶与异常情况。

（十）活动报告

1.报告时机：在下列活动开始前和结束后：

1.1拆修主机、锅炉、锚机、舵机；

1.2试航、试车、校正磁罗经；

1.3放艇（筏）。

2.报告：珠海交管中心

3.报告方式：VHF CH13

4.报告内容：船舶（船名、呼号）、船位和其他信息。

三、引航

（一）引航报告

1.报告时机：引航员登离轮。

2.报告：珠海交管中心

3.报告方式：VHF CH13

4.报告内容：船舶（船名、呼号）、时间等。

（二）强制引航船舶

1.外国籍船舶；

2.法律、行政法规规定应当申请引航的中国籍船舶。

（三）引航员登离点

1.大型船舶登（离）点：（吃水≥13.0米或船长≥250米）

21°47′.70N/113°15′.40E。

2.大中型船舶登（离）点：（吃水＜13.0米且船长＜250米）

21°50′.20N/113°14′.00E。

3.小型船舶登（离）点（进出新会）：（船长≤120米）

21°53′.50N/113°11′.50E。

4.小型船舶登（离）点（进出高栏）：（船长≤120米）

21°53′.50N/113°12′.80E。

四、提供的服务

（一）信息服务

应船舶请求，提供他船动态、助航标志、水文气象、航行警（通）告信息服务。

（二）助航服务

应船舶请求，协助船舶定位，但不向船舶发出具体航行指令。（三）交通组织服务。

五、获取信息途径

珠海VTS中心：

通信地址：珠海市吉大情侣中路15号1栋

邮政编码：519015

联系电话：+86-756-3339454

传    真：+86-756-3371737

电邮地址：zhvts@gdmsa.gov.cn

VHF工作语言：汉语普通话、英语

工作时间：00:00-24:00（北京时间）

Vessel Traffic Services Guide

– (China) – (Zhuhai VTS)

1. VHF Procedures

1.1 SECTOR:

Zhuhai VTS area consists of 1 sector:

Sector                     Working channel

Zhuhai                 Calling/Watching Channel VHF CH13

Service Channel VHF CH68/ CH08

Vessels should call Zhuhai VTS and maintain a continuous listening watch on the appropriate VHF Channel.

1.2 Other port user channels:

Tugs         VHF CH16 or VHF CH13

Pilot         VHF CH16 or VHF CH13

1.3. VTS Area:

There are four reporting lines in Zhuhai VTS area:

1.3.1 Western Reporting Line: starting from 21°45'N/113°07'E along longitude 113°07'E towards north to coast line;

1.3.2 Southern Reporting Line: starting from 21°45'N/113°07'E along latitude 21°45′N towards east to 21°45'N/113°27' E;

1.3.3 Eastern Reporting Line: starting from 21°45'N/113°27'E along longitude 113°27'E towards north to 21°59'N/113°27' E;

1.3.4 Northern Reporting Line: starting from 21°59'N/113°27' E to 21°54'N/113°16' E;

2. Reports

2.1 Applicability:

Zhuhai VTS system is MANDATORY and applies to the following vessels. All these vessels MUST apply for permission to enter the waters of Zhuhai VTS.

2.1.1 Foreign flagged vessels or facilities;

2.1.2 Chinese flagged vessels ≥ 500GT;

2.1.3 Passenger vessels with a carrying capacity of ≥ 30 passengers;

2.1.4 Vessels carrying dangerous cargo;

2.1.5 Vessels constrained by her manoeuvring ability.

2.2 Pre-entry Report(Only Vessels ≥ 1000 GT expected entry to the VTS Waters)

WHEN: 24 hours before the intended entry (or on her departure from the last port of call if the voyage takes less than 24 hours)

TO:   Zhuhai VTS CENTER

VIA:  Written report (including FAX,e-form submission or e-mail)

GIVING: VTS Vessel Dynamic Plan Guide

2.3 Entry Report

WHEN:  Passing the VTS reporting line (point) and/or approaching the berth or anchorage.(LNG vessels should report arrival time to VTS center 2 hours before arriving at VTS reporting line)

TO:    Zhuhai VTS CENTER

VIA:   VHF CH13

GIVING: IMO SRS Items: Alpha Charlie

2.4 Arrival Report

WHEN: Anchoring, mooring floats or securing to a berth within VTS waters.

TO:    Zhuhai VTS CENTER

VIA:   VHF CH13

GIVING: IMO SRS Item: Alpha Bravo Charlie

2.5 Pre-move and Pre-departure Report

WHEN: Before moving or departing.

TO:    Zhuhai VTS CENTER

VIA:    CH13

GIVING: IMO SRS Items: Alpha Bravo Charlie India

2.6 Outbound Report

WHEN: Passing VTS reporting line (point) and/or departing from the VTS area.

TO:    Zhuhai VTS CENTER

VIA:   VHF CH13

GIVING: IMO SRS ITEMS: Alpha Bravo (Departure time/time passing report line) Charlie

2.7 Deviation Reports

WHEN: Any change in details given in the pre-entry report

TO:    Zhuhai VTS CENTER

VIA:   VHF CH13

GIVING: Any changed information

2.8 Incident Report

WHEN: All vessels shall immediately report any incident impairing safety or the environment.

TO:    Zhuhai VTS CENTER

VIA:   VHF CH13

GIVING: Full details of the incident

2.9 Observations Report

WHEN: Observing any conditions that may affect the safety of navigation.

TO:    Zhuhai VTS CENTER

VIA:    VHF CH13

GIVING: IMO SRS Items: Alpha X-ray (Navigational status and any accidents

and/or damage occurred during navigation).

2.10 Activities Reports

WHEN: Before or after carrying out any of the following operations:

2.10.1 Overhauling main engines, boilers, anchor windlass, steering engines;

2.10.2 Testing main engines, ship trials or calibrating magnetic compass;

2.10.3 Launching of vessel’s lifeboat or life-raft.

TO:     Zhuhai VTS CENTER

VIA:    VHF CH13

GIVING: IMO SRS Items: Alpha Charlie X-ray.

3. Pilotage

3.1 Pilot Report

WHEN: Pilot embarking or disembarking.

TO:    Zhuhai VTS CENTER

VIA:   VHF CH13

GIVING: IMO SRS Items: Alpha Bravo

3.2 Pilotage is compulsory for:

3.2.1 Foreign flagged vessels;

3.2.2 Chinese flagged vessels which should apply for pilotage under provisions of laws and administrative regulations.

3.3 Pilot boarding stations (PBS)

3.3.1 Large sized ships(LOA≥250meters or Maximum Draught≥13.0meters):21o47'.70N/113o15'.40E;

3.3.2 Middle to large sized ships (LOA<250meters and Maximum Draught<13.0meters): 21o50'.20N/113o14'.00E;

3.3.3 Small sized ships (bound or outward bound for Xinhui): 21o53'.50N/113o11'.50E;

3.3.4 Small sized ships (bound or outward bound for Gaolan): 21o53'.50N/113o12'.80E.

4. Services Offered

4.1 Information Service (INS)

Providing other vessels’ dynamic status, navigation aids, hydrometeorology, navigation warning (notice) information service on ship’s request.

4.2 Navigational Assistance Service (NAS)

Assisting vessels with location without specific navigation instruction on ship’s request.

4.3 Traffic Organization Service (TOS)

5. Information Inquiry

Contact details of Zhuhai VTS Center:

Address: Building 1, No.15Middle Qinglv Road, Zhuhai, Guangdong, P.R.China

Post Code: 519015

Tel: +86-756-3339454

Fax: +86-756-3371737

E-mail: zhvts@gdmsa.gov.cn

Working Languages: Mandarin/English

Service Time: 00:00-24:00(Beijing time)